## Slide 1: Lithogeochemistry in exploration for intrusion-hosted magmatic Ni-Cu-Co-PGE deposits: identifying cumulate rocks and chalcophile element backgrounds
Steve Barnes V1.0 May 2022
Mineral Resources

## Slide 2
~100 m of channel-fill cover
What do we want lithogeochemistry to do?…
Reliable inference from geographically sparse data sets
Notes: It is well known that most of the surface deposits have already been found.
Australia specifically has large sections that are undercover
How will we find new nickel deposits?
I think indicator minerals can help

## Slide 3
Prediction
“Fertility” – fertile magma suites
Favourable tectonic/magmatic settings
Detection
Distal indicators – edges of mineral systems
Vectors within mineral systems
We want them to be
Routine, easily collectable reproducible data
Minimal false positives, false negatives
What do we want geochemical exploration tools to do?…
Reliable inference from geographically sparse data sets
Notes: It is well known that most of the surface deposits have already been found.
Australia specifically has large sections that are undercover
How will we find new nickel deposits?
I think indicator minerals can help

## Slide 4
If we’ve only got THIS
Can we predict presence of THIS

## Slide 5
Immiscible sulfide liquid forms via assimilation of S-rich wall rocks
1
+S
+S
Magma
in
Droplets (now enriched with metals) separate from magma and form deposit.
3
Magma
out
Sulfide droplets mix with magma & scavenge metals
2
Sulfide differentiation, migration, recycling, sulfide-silicate interactions
4

## Slide 6
Identifying cumulates
(especially ultramafic)
Chalcophile depletion
in outflow
Trace CPE enrichment halo in flanking sills
Kalatongke, NW China
Barnes et al., OGR, 2016

## Slide 7
Deposition sites are characterised by the presence of cumulates – usually but not always ultramafic cumulates.

## Slide 8: Cumulate rocks – what are they?
The solid products of fractional crystallisation of magmas
magma1
magma2 + crystals
magma2
cumulates
cooling
+
Products of sorting of crystals from magmas

## Slide 9
Most of the cumulate rocks we find in ore-hosting intrusions can be explained by reference to phase relations in a four component system-
Olivine (Forsterite) – Clinopyroxene (Diopside) – Plagioclase (Anorthite) – Silica

## Slide 10
Most of the cumulate rocks we find in ore-hosting intrusions can be explained by reference to phase relations in a four component system-
Olivine (Forsterite) – Clinopyroxene (Diopside) – Plagioclase (Anorthite) – Silica

## Slide 11
Olivine-cpx cycles
olivine
Olivine
Cpx
Plag
Olivine-cpx cumulate layering, Munni Munni
Ol cumulates
Olivine + Cpx
Ol + Cpx cumulates
Ol gabbro
(Ol+Plag+Cpx)
Olivine-cpx cycles
Oscillatory-zoned cpx in cpx-olivine cumulate, Kevitsa, Finland

## Slide 12
Olivine-cpx cycles
olivine
Olivine
Cpx
Plag
Messages:
A small change in the parent magma composition can produce a really big change in the major-element composition of the cumulates
This can also result in big changes in the compatible trace elements
Ultramafic cumulates don’t require ultramafic magmas
Ol cumulates
Olivine + Plag
Ol + Plag cumulates
Ol gabbro
(Ol+Plag+Cpx)

## Slide 13
Add silica
Olivine + Plag
Troctolite – signature rock type of Voisey’s Bay

## Slide 14
Adding silica during contamination commonly causes mafic magmas to crystallise orthopyroxene (enstatite) instead of olivine.
Poikilitic
Harzburgite
Norite

## Slide 15
Add silica
Dynamic contamination  opx cumulates, “oikocrystites”, complex Cr zoning.
Ntaka, Tanzania. Barnes et al., 2016, J Pet. doi:10.1093/petrology/egw036

## Slide 17
In a cumulate rock, the cumulus mineralogy determines the whole rock composition.
In a non-cumulate rock, the bulk composition determines the mineralogy
Orthocumulate, ~50% trapped liquid
Adcumulate, <5% trapped liquid
Orthocumulates are somewhere in between
Mixture of cumulus mineral plus liquid compositions
Olivine + liquid
Liquid crystallises to form intercumulus phases, + overgrowth on cumulus phases

## Slide 18
Standard Geochem two-oxide plots
Opx-bearing
Opx-bearing
Opx-bearing
Olivine cumulates
Olivine cumulates
Olivine cumulates
Olivine cumulates
Mafic cumulates
Mafic cumulates
Mafic cumulates
Mafic cumulates
Mafic non-cumulates
(fractionated liquids)
Mafic non-cumulates
Mafic non-cumulates
Mafic non-cumulates
Big overlap between mafic cumulates and non-cumulates

## Slide 19: Lithogeochem discrimination of cumulates
Mg# = Mg/(Mg+Fe) (molar values)
Mg mol = MgO/40.3,
Fe mol = FeO/71.9
Savannah (Sally Malay)
Variation due to increasing proportion of intercumulus liquid
Cumulus olivine + sulfide + silicate liquid
Cumulus olivine + sulfide + intercumulus minerals
Cumulates are mixtures of
Cumulus minerals (olivine, pyroxene, plag, sulfide liquid
Intercumulus silicate liquid
Variation due to different proportions of cumulus plagioclase to olivine +pyroxene
Most potential targets contain a high proportion of olivine or olivine+pyroxene cumulates.
Which ones don’t? Norilsk and Voisey’s Bay…

## Slide 20: Lithogeochem discrimination of cumulates
Mg# = Mg/(Mg+Fe) (molar values)
Mg mol = MgO/40.3,
Fe mol = FeO/71.9
Savannah (Sally Malay)
Same data, alteration-robust “pXRF elements”
Peridotites (olivine cumulates)
Pyroxenites

## Slide 21
Ntaka Hill (Tanzania – high Mg basalt parent magma)
Some igneous-textured pyroxenites and peridotites
(very few plag cumulates)
Mostly metamorphic amphibolite/metapyroxenite
Opxnite cumulates
Non-cumulates

## Slide 22: Nova
Host intrusion
Ol+Opx
orthocumulates
Norite/G’norite cumulates
Very small proportion of non-cumulate rock

## Slide 23
Mg# vs Al/Ti plots
Ultramafic cumulate – no plag, therefore should have same Al/Ti as parent magma (not exact due to presence of Al in spinel, pyroxene)
Accumulation of plagioclase
Fractional crystallisation of plagioclase + px/ol
Mantle value

## Slide 24
Albany-Fraser Orogen, Fraser Zone Nova
UM-c
Maf-c
Maf non-c
UM-c
Maf-c
Maf non-c

## Slide 25
Kimberley- Halls Creek Orogen Savannah
UM-c
Maf-c
Maf non-c
UM-c
Maf-c
Maf non-c

## Slide 26
MozMB - Ntaka
UM-c
Maf-c
Maf non-c
UM-c
Maf-c
Maf non-c

## Slide 27
Kimberley - Hart Dolerite
UM-c
Maf-c
Maf non-c
UM-c
Maf-c
Maf non-c

## Slide 28
Summary:
identifying cumulate-dominant units picks out host intrusions
Sill complexes dominated by non-cumulates are low-potential targets

## Slide 29
Caveat: some closed-system intrusions can contain low Mg# cumulates from highly fractionated liquids. Identify with incompatible elements – Zr, Ti
Intrusions with a high proportion of these rocks are generally less prospective.
Message: multi-variate data needs multiple discriminants – no simple “dartboards”
Weight of evidence approach is needed

## Slide 30
Caveat: some closed-system intrusions can contain low Mg# cumulates from highly fractionated liquids. Identify with incompatible elements – Zr, Ti
Intrusions with a high proportion of these rocks are generally less prospective.
Message: multi-variate data needs multiple discriminants – no simple “dartboards”
Weight of evidence approach is needed

## Slide 31: Olivine or orthopyroxene cumulates?
Triangular plots using molar proportions
Mg+Fe mol = MgO/40.3 + FeO/71.9 Si mol = SiO2/60.1 Al mol = Al2O3/51

## Slide 32
Formulae for calculating molar components from whole rock geochemical analyses
Mg mol MgO/40.3
Fe mol [Total Fe as FeO*]/71.9
Si mol SiO2/60.1
Al mol Al2O3/51
Ti mol TiO2/79.9
Mg# Mg mol/[Mg mol + Fe mol]

## Slide 33
The diagrams shown here are available as IoGas Diagram templates. You will need the following columns, named exactly as shown: MgO_pct, Al2O3_pct, SiO2_pct, FeO_pct, Mg# mol pct, TiO2_pct.
Download the zip file and save the individual xml files to:
C:\Users\USERNAME\AppData\Roaming\ioGAS\cache\iod\DiagramAndCalc

## Slide 34: Identifying cumulus phases from Lithochem Conserved element ratios
(Nova data from Taranovic et al., Econ Geol 2022)
Method for recognising accumulation of olivine, pyroxene, plagioclase
Process: calculate molar MgO, FeO, SiO2 (oxide weight pct/molecular weight)
MgO/40.3 = m
FeO/71.9 = f
SiO2/60.1 = s
Divide by oxide/mol.wt of a component excluded from all these phases – Ti is ideal,
TiO2/79.9 = t
Plot s/t vs (m=f)/t
Olivine has formula (Mg,Fe)2SiO4 so addition of olivine produces a line with slope 0.5 (adding one mole of Si for every 2 of Mg+Fe
Opx is (Mg,Fe) SiO3 so addition produces a line with slope =1
Adding pyroxene = plagioclase in cotectic proportion produces slope ~=2

## Slide 35: Identifying cumulus phases from Lithochem - Conserved element ratios
(Nova data from Taranovic et al., Econ Geol 2022)
Method for recognising accumulation of olivine, pyroxene, plagioclase
Process: calculate molar MgO, FeO, SiO2 (oxide weight pct/molecular weight)
MgO/40.3 = m
FeO/71.9 = f
SiO2/60.1 = s
Divide by oxide/molwt of a component excluded from all these phases – Ti is ideal,
TiO2/79.9 = t
Plot s/t vs (m=f)/t
Olivine has formula (Mg,Fe)2SiO4 so addition of olivine produces a line with slope 0.5 (adding one mole of Si for every 2 of Mg+Fe
Opx is (Mg,Fe) SiO3 so addition produces a line with slope =1
Adding pyroxene = plagioclase in cotectic proportion produces slope ~=2
Position along line depends on trapped liquid proportion – low=adcumulate, high=orthocumulate
More adcumulate
More orthocumulate

## Slide 36: Identifying cumulus phases from Lithochem Conserved element ratios
Slope = 1 (opx)
Ntaka (pyroxenite host)
Lower (host) intrusion at Nova –
slope = 0.8 (oliv + opx)
Full details: Stanley and Russell 1989 CTMP DOI:10.1007/BF00371366

## Slide 37
Lithogeochemistry in weathered materials – what can we use?

## Slide 38
Lithogeochemistry in weathered materials – what can we use?
Ratios of any of these elements – e.g. Ni-Cr-Ti triangular plot - can be used in saprock or altered rock
“Saprock” (typical TOFR in RC holes)

## Slide 39: Lithogeochem discrimination of trace cumulate sulfide
Cumulus olivine + sulfide + silicate liquid
Cumulus olivine + sulfide + intercumulus minerals
Cumulates are mixtures of
Cumulus minerals (olivine, pyroxene, plag, sulfide liquid
Intercumulus silicate liquid
Intercumulus liquid might contain (say) 500 ppm S, 200 ppm Cu
So an olivine orthocumulate (50% liquid) has 250 ppm S, 100 ppm Cu
So what is an anomaly?

## Slide 40: Lithogeochem discrimination of trace cumulate sulfide
Cumulus olivine + sulfide + silicate liquid
Cumulus olivine + sulfide + intercumulus minerals
Look for
Anomalous high Ni (but silicate Ni background is highly variable
Low level Pt-Pd (corrected for cumulus/trapped liquid proportion)
Anomalous Cu (but can be highly mobile in altered rocks) – also has trapped liquid effect

## Slide 41
Mafic-ultramafic rocks in Proterozoic mobile belts
Mantle ratio
Depleted due to sulfide extraction
Enriched due to sulfide addition
Enriched due to sulfide addition

## Slide 42
Remove the purple M&Ms – the concentration of the yellow and blue ones increases but their PROPORTION stays the same
So Cu/Zr unaffected by silicate fractionation

## Slide 43
Albany-Fraser
Nova
DEPLETED
ENRICHED

## Slide 44
Halls Creek
Savannah
Hart Dolerite

## Slide 45
Albany-Fraser
Nova
Crustal contamination
Combine Cu/Zr with trace element ratio proxies for crustal contamination – e.g. Th/Nb
mantle
mantle
Sulfide addition

## Slide 46
Halls Creek
Savannah
Hart Dolerite
Crustal contamination
Pr-mantle
Pr-mantle
Kimberley, WA

## Slide 47
Ntaka (Mozambique Belt)
Crustal contamination
mantle
mantle

## Slide 48: Why can’t we just look for Ni anomalies?
Prot. mobile belt data (all)

## Slide 49
Prot. mobile belt data (Cu- and Cu-Ni anomalous rocks removed)
Opx cumulates
Olivine cumulates
Gabbros, troctolites

## Slide 50: What is the threshold for anomalous Ni in an ultramafic rock?
Ntaka, Tanzania (high-Mg basalt parent magma)
Samples with >0.5% S

## Slide 51
Can we use PGEs?
51
 Example at Long Victor, Kambalda:
Enriched
Depleted
Nancy SGA2015 workshop Aug. 2015 I Margaux Le Vaillant
Work well in komatiites. Subtle positive and negative anomalies in PGE (Pd-Pt in particular) in komatiite host units (100’s m scale vectoring) using ratios Pt/Ti, Pd/Ti (invariant to olivine fractionation)
Heggie et al., 2012 Econ Geol
Barnes et al., 2013 Econ Geol
Can we do the same in mafic systems?
Enrichment due to trace sulfide
Depletion due to sulfide extraction

## Slide 52
Pt/Ti
Pd/Ti
Can we use PGEs in mafic systems? Difficult due to wide variability in background
Komatiites consistent, mainly undepleted
Basalts widely variable – Sulfides in source