## Slide 1: Spark
May 2023

## Slide 2: Introduction
Need to simulate wildfires for risk modelling and operational management
Given:
Ignition conditions (points, lines or areas)
Information on the fuel and landscape
Weather data
Firebreaks and suppression
We need:
Where the fire will go
The intensity of the fire
Heat flux on structures
Where firebrands will land
…
All of these elements must be included in a computer model
Computer model must be rapid enough for operational prediction
Rate-of-spread

## Slide 3: Introduction
The rate-of-spread depends on:
The type of fuel
The condition of the fuel (amount, moisture level, …)
Empirical rate of spread models developed from experiments
Mathematical function for rate-of-spread
Need to use many different models for fire prediction
Each model may require different data
Spinifex fire. Source: NASA Earth Observatory
Eucalypt fire. Source: RMIT

## Slide 4: Introduction
In addition to the rate of spread the following must also be considered:
Terrain - fires move faster uphill
Local wind effects - channelling and lateral spread
Smoke - long range effect
‘Near-field’ - fire interacts with itself
Radiation - cause structure damage
Firebrands - create unpredictable new fires
Ongoing worldwide research into all of these areas

## Slide 5: Spark
Spark is a wildfire prediction framework:
Based on configurable scripts wherever possible
Rate-of-spread based on input data – wind, fuel, terrain
Compatibility with all common geospatial data types
Plug-ins for firebrands, radiant heat flux, terrain, fire feedback
Python-based for further customisation
Web front end (SparkWeb) and server (Spark server)
SparkWeb
Spark server
Geostack
Spark

## Slide 6: Modelling
Computational wildfire models:
Front tracking
Cellular
Front tracking
Represents perimeter as line
Very efficient to update node positions
Need to filter nearby points
Lines can get tangled after update/merging
Cellular methods
Domain is a set of cells
Fire spreads from cell to cell
Extremely efficient processing
Cell geometry affects simulation

## Slide 7: Modelling
Spark model
Level set method:
Precise control of rate-of-spread in each cell
Automatically handles merging fires
Efficient and scalable on new computer hardware
Models:
Defined using scripts, not hard-coded
Inputs and output layers can be referenced and used
All projections, spatial and temporal sampling transparently handled
Script for grassland fires in Spark
Level set method

## Slide 8: Data
‘elevation’
‘fuel_load’
‘curing’
Forest model
RoS(elevation, fuel load)
Grassland model
Ros(elevation, curing)
Other models
Any combination of input spatial layers
Any user-defined variables, layers or series can be used
System handles spatial and temporal sampling
Integration to support any geospatial data type

## Slide 9: SparkWeb

## Slide 10: SparkWeb
Usage
Authentication required

## Slide 11: SparkWeb
Usage
Authentication required
Terms of use

## Slide 12: SparkWeb
Usage
Authentication required
Terms of use
Create a new project

## Slide 13: SparkWeb
Usage
Authentication required
Terms of use
Create a new project

## Slide 14: SparkWeb
Usage
Authentication required
Terms of use
Create a new project
  Projects must be named
  Pre-populated templates

## Slide 15: SparkWeb
Usage
Authentication required
Terms of use
Create a new project
  Projects must be named
  Pre-populated templates
Layer panel on right-hand side

## Slide 16: SparkWeb
Usage
Authentication required
Terms of use
Create a new project
  Projects must be named
  Pre-populated templates
Layer panel on right-hand side
Fire input conditions
  Tools on lower left
  Point tool

## Slide 17: SparkWeb
Usage
Authentication required
Terms of use
Create a new project
  Projects must be named
  Pre-populated templates
Layer panel on right-hand side
Fire input conditions
  Tools on lower left
  Point tool
Basic simulation parameters

## Slide 18: SparkWeb
Usage
Authentication required
Terms of use
Create a new project
  Projects must be named
  Pre-populated templates
Layer panel on right-hand side
Fire input conditions
  Tools on lower left
  Point tool
Basic simulation parameters
  Start date and time
  Time zone
  Simulation duration
  Simulation resolution
Project controls
  Run
  Save
  Download

## Slide 19: SparkWeb
Usage
Authentication required
Terms of use
Create a new project
  Projects must be named
  Pre-populated templates
Layer panel on right-hand side
Fire input conditions
  Tools on lower left
  Point tool
Basic simulation parameters
  Start date and time
  Time zone
  Simulation duration
  Simulation resolution
Project controls
  Run
  Save
  Download
Progress
  Any errors reported at this stage

## Slide 20: SparkWeb
Usage
Authentication required
Terms of use
Create a new project
  Projects must be named
  Pre-populated templates
Layer panel on right-hand side
Fire input conditions
  Tools on lower left
  Point tool
Basic simulation parameters
  Start date and time
  Time zone
  Simulation duration
  Simulation resolution
Project controls
  Run
  Save
  Download
Progress
  Any errors reported at this stage
Output of fire simulation
  Colours represent hourly progress

## Slide 21: SparkWeb
Results and visualisation
Layers
  List on right-hand side
  Visibility controlled by view icons
Shaded fire contour
  Dynamic outline based on time slider

## Slide 22: SparkWeb
Results and visualisation
Layers
  List on right-hand side
  Visibility controlled by view icons
Shaded fire contour
  Dynamic outline based on time slider
Wildfire model layer
  Cell evaluation using inspection tool
  Current value of all layers under mouse

## Slide 23: SparkWeb
Results and visualisation
Layers
  List on right-hand side
  Visibility controlled by view icons
Shaded fire contour
  Dynamic outline based on time slider
Wildfire model layer
  Cell evaluation using inspection tool
  Current value of all layers under mouse
Flame height layer

## Slide 24: SparkWeb
Results and visualisation
Layers
  List on right-hand side
  Visibility controlled by view icons
Shaded fire contour
  Dynamic outline based on time slider
Wildfire model layer
  Cell evaluation using inspection tool
  Current value of all layers under mouse
Flame height layer
Base map
  Various base map options

## Slide 25: SparkWeb
Results and visualisation
Layers
  List on right-hand side
  Visibility controlled by view icons
Shaded fire contour
  Dynamic outline based on time slider
Wildfire model layer
  Cell evaluation using inspection tool
  Current value of all layers under mouse
Flame height layer
Base map
  Various base map options
3D view
  Right mouse or ctrl+left mouse to rotate view
  Mousewheel to zoom
  View reset using compass button

## Slide 26: SparkWeb
Results and visualisation
Layers
  List on right-hand side
  Visibility controlled by view icons
Shaded fire contour
  Dynamic outline based on time slider
Wildfire model layer
  Cell evaluation using inspection tool
  Current value of all layers under mouse
Flame height layer
Base map
  Various base map options
3D view
  Right mouse or ctrl+left mouse to rotate view
  Mousewheel to zoom
  View reset using compass button
Layer options
  Layer download buttons
  Opacity slider
  Colour map
  Colour range
Layer download

## Slide 27: SparkWeb
Results and visualisation
Layers
  List on right-hand side
  Visibility controlled by view icons
Shaded fire contour
  Dynamic outline based on time slider
Wildfire model layer
  Cell evaluation using inspection tool
  Current value of all layers under mouse
Flame height layer
Base map
  Various base map options
3D view
  Right mouse or ctrl+left mouse to rotate view
  Mousewheel to zoom
  View reset using compass button
Layer options
  Layer download buttons
  Opacity slider
  Colour map
  Colour range
Layer download
Weather
  Changes with time slider

## Slide 28: SparkWeb
Results and visualisation
Layers
  List on right-hand side
  Visibility controlled by view icons
Shaded fire contour
  Dynamic outline based on time slider
Wildfire model layer
  Cell evaluation using inspection tool
  Current value of all layers under mouse
Flame height layer
Base map
  Various base map options
3D view
  Right mouse or ctrl+left mouse to rotate view
  Mousewheel to zoom
  View reset using compass button
Layer options
  Layer download buttons
  Opacity slider
  Colour map
  Colour range
Layer download
Weather
  Changes with time slider
  Shows time series chart when icon is clicked

## Slide 29: SparkWeb
Results and visualisation
Layers
  List on right-hand side
  Visibility controlled by view icons
Shaded fire contour
  Dynamic outline based on time slider
Wildfire model layer
  Cell evaluation using inspection tool
  Current value of all layers under mouse
Flame height layer
Base map
  Various base map options
3D view
  Right mouse or ctrl+left mouse to rotate view
  Mousewheel to zoom
  View reset using compass button
Layer options
  Layer download buttons
  Opacity slider
  Colour map
  Colour range
Layer download
Weather
  Changes with time slider
  Shows time series chart when icon is clicked
  Can be downloaded as a csv

## Slide 30: SparkWeb
Advanced usage
Weather inputs
  Spark requires whatever weather variables your rate of spread models use as inputs
  Generally wind speed and direction, relative humidity and temperature
  Could also include drought factor, dew temperature, curing
  Can be uploaded as a set of gridded netcdf files

## Slide 31: SparkWeb
Advanced usage
Weather inputs
  Spark requires whatever weather variables your rate of spread models use as inputs
  Generally wind speed and direction, relative humidity and temperature
  Could also include drought factor, dew temperature, curing
  Can be uploaded as a set of gridded netcdf files
  Or a suitable weather csv file can be dragged and dropped into the ‘Simulation series CSV’ input
  Example csv format:

## Slide 32: SparkWeb
Advanced usage
Input tools
  Point fire creation
  Line fire creation
  Polygon fire creation
  Mask (un-burnable) creation

## Slide 33: SparkWeb
Advanced usage
Input tools
  Point fire creation
  Line fire creation
  Polygon fire creation
  Mask (un-burnable) creation
Multiple geometries
  Different start times

## Slide 34: SparkWeb
Advanced usage
Input tools
  Point fire creation
  Line fire creation
  Polygon fire creation
  Mask (un-burnable) creation
Multiple geometries
  Different start times
  Left-click to configure
  Set geometry properties
  Set ignition time
  Set position

## Slide 35: SparkWeb
Advanced usage
Advanced options
  All layers and options available

## Slide 36: SparkWeb
Advanced usage
Advanced options
  All layers and options available
Layers

## Slide 37: SparkWeb
Advanced usage
Advanced options
  All layers and options available
Layers
  Vector layers
  Gridded weather layers (NetCDF)
  Output layers, any with descriptions are visualised

## Slide 38: SparkWeb
Advanced usage
Advanced options
  All layers and options available
Layers
  Vector layers
  Gridded weather layers (NetCDF)
  Output layers, any with descriptions are visualised
Models
  Initialisation, run once per cell

## Slide 39: SparkWeb
Advanced usage
Advanced options
  All layers and options available
Layers
  Vector layers
  Gridded weather layers (NetCDF)
  Output layers, any with descriptions are visualised
Models
  Initialisation, run once per cell
  Advection, used to modify wind field
  Rate-of-spread, run to determine outward speed

## Slide 40: SparkWeb
Advanced usage
Advanced options
  All layers and options available
Layers
  Vector layers
  Gridded weather layers (NetCDF)
  Output layers, any with descriptions are visualised
Models
  Initialisation, run once per cell
  Advection, used to modify wind field
  Rate-of-spread, run to determine outward speed
  Update, run within burnt regions

## Slide 41: SparkWeb
Advanced usage
Advanced options
  All layers and options available
Layers
  Vector layers
  Gridded weather layers (NetCDF)
  Output layers, any with descriptions are visualised
Models
  Initialisation, run once per cell
  Advection, used to modify wind field
  Rate-of-spread, run to determine outward speed
  Update, run within burnt regions
Reductions
  Reduces output to single value
  Set per-layer
  Value shown in summary table

## Slide 42: SparkWeb
Advanced usage
Layer creation
  Any number can be created
  Name available in model scripts for reading/writing
  Must have description to be visualised
  Example ‘test’ layer created called ‘Test’

## Slide 43: SparkWeb
Advanced usage
Layer creation
  Any number can be created
  Name available in model scripts for reading/writing
  Must have description to be visualised
  Example ‘test’ layer created called ‘Test’
Scripting
  Layer is written in update model
  Anywhere where flame height > 3 test is 1
  Elsewhere test is null

## Slide 44: SparkWeb
Advanced usage
Layer creation
  Any number can be created
  Name available in model scripts for reading/writing
  Must have description to be visualised
  Example ‘test’ layer created called ‘Test’
Scripting
  Layer is written in update model
  Anywhere where flame height > 3 test is 1
  Elsewhere test is null
Visualisation
  Data from ‘Test’ shown in green after simulation is run again

## Slide 45: SparkWeb
Advanced usage
Layer creation
  Any number can be created
  Name available in model scripts for reading/writing
  Must have description to be visualised
  Example ‘test’ layer created called ‘Test’
Scripting
  Layer is written in update model
  Anywhere where flame height > 1 test is 1
  Elsewhere test is null
Visualisation
  Data from ‘Test’ shown in green after simulation is run again
Errors
  Errors appear in a red box
  Script errors trigger ‘Spark simulation failed’
  Reported as a ‘clBuildProgram: -11’ exception
  We will make this more intelligible!
  The full error log is available in the API response

## Slide 46: SparkWeb
Advanced usage
Rate-of-spread scripts
  Script for each fuel classification type
  Each type is an integer identifier ‘class’
  Zero is reserved for un-burnable
  Classes can be named

## Slide 47: SparkWeb
Advanced usage
Rate-of-spread scripts
  Script for each fuel classification type
  Each type is an integer identifier ‘class’
  Zero is reserved for un-burnable
  Classes can be named
Example 1
  Script “speed = 0.5;”
  Sets outward speed to 0.5 m/s
  Resulting fire is circular

## Slide 48: SparkWeb
Advanced usage
Rate-of-spread scripts
  Script for each fuel classification type
  Each type is an integer identifier ‘class’
  Zero is reserved for un-burnable
  Classes can be named
Example 1
  Script “speed = 0.5;”
  Sets outward speed to 0.5 m/s
  Resulting fire is circular
Example 2
  Script “speed = 0.1+0.02*wind;”
  Adds component in wind direction
  Resulting fire grows outwards and moves with wind

## Slide 49: SparkWeb
Advanced usage
Firebrand model
  McArthur firebrand model
  Requires script to determine creation

## Slide 50: SparkWeb
Advanced usage
Firebrand model
  McArthur firebrand model
  Requires script to determine creation
Sub models
  Currently only firebrand transport model
Firebrand model
  Models for all firebrand stages
  Creation script, sets new firebrand positions
  Initialisation script, creates firebrands
  Advection model, controls air flow
  Update model, controls firebrand changes
  Transport model, controls interaction with air flow
  Basic spot fire creation only required one model

## Slide 51: SparkWeb
Advanced usage
Firebrand model
  McArthur firebrand model
  Requires script to determine creation
Sub models
  Currently only firebrand transport model
Firebrand model
  Models for all firebrand stages
  Creation script, sets new firebrand positions
  Initialisation script, creates firebrands
  Advection model, controls air flow
  Update model, controls firebrand changes
  Transport model, controls interaction with air flow
  Basic spot fire creation only required one model
Visualisation
  Firebrands which cause spot fires are visualised with yellow lines from generation to landing points

## Slide 52: SparkWeb
Advanced usage
Uploading user data layers
  Note, the wildfire platform is currently open. Do not upload any sensitive data as other users will be able to use it. Please use specific filenames to ensure no duplicates (e.g. MY_USER_land_classification_EPSG_XXXX_v1.tiff)

## Slide 53: SparkWeb
Advanced usage
Uploading user data layers
  Note, the wildfire platform is currently open. Do not upload any sensitive data as other users will be able to use it. Please use specific filenames to ensure no duplicates (e.g. MY_USER_land_classification_EPSG_XXXX_v1.tiff)
  File is uploaded with the path: /geowebfs/uploads/FILENAME
  Input the correct projection and data type as well as a name which can be referred to in the model scripts.

## Slide 54: SparkWeb
Advanced usage
Uploading user data layers
  Note, the wildfire platform is currently open. Do not upload any sensitive data as other users will be able to use it. Please use specific filenames to ensure no duplicates (e.g. MY_USER_land_classification_EPSG_XXXX_v1.tiff)
  File is uploaded with the path: /geowebfs/uploads/FILENAME
  Input the correct projection and data type as well as a name which can be referred to in the model scripts.
Visualising user data layers
  Create an output layer

## Slide 55: SparkWeb
Advanced usage
Uploading user data layers
  Note, the wildfire platform is currently open. Do not upload any sensitive data as other users will be able to use it. Please use specific filenames to ensure no duplicates (e.g. MY_USER_land_classification_EPSG_XXXX_v1.tiff)
  File is uploaded with the path: /geowebfs/uploads/FILENAME
  Input the correct projection and data type as well as a name which can be referred to in the model scripts.
Visualising user data layers
  Create an output layer
  Write to the output in a model script

## Slide 56: SparkWeb
Advanced usage
Uploading user data layers
  Note, the wildfire platform is currently open. Do not upload any sensitive data as other users will be able to use it. Please use specific filenames to ensure no duplicates (e.g. MY_USER_land_classification_EPSG_XXXX_v1.tiff)
  File is uploaded with the path: /geowebfs/uploads/FILENAME
  Input the correct projection and data type as well as a name which can be referred to in the model scripts.
Visualising user data layers
  Create an output layer
  Write to the output in a model script
  Run simulation again to view output
  Your layer name can be used in Initialisation, Rate of Spread and Update models

## Slide 57: SparkWeb
Advanced usage
Uploading user data layers
  Note, the wildfire platform is currently open. Do not upload any sensitive data as other users will be able to use it. Please use specific filenames to ensure no duplicates (e.g. MY_USER_land_classification_EPSG_XXXX_v1.tiff)
  File is uploaded with the path: /geowebfs/uploads/FILENAME
  Input the correct projection and data type as well as a name which can be referred to in the model scripts.
Visualising user data layers
  Create an output layer
  Write to the output in a model script
  Run simulation again to view output
  Your layer name can be used in Initialisation, Rate of Spread and Update models

## Slide 58: SparkWeb
Spark server
Web API
  Services calls from SparkWeb
  Can be called directly to run simulations/serve outputs
  All models sent to server

## Slide 59: SparkWeb
Spark server
Web API
  Services calls from SparkWeb
  Can be called directly to run simulations/serve outputs
  All models sent to server
API calls
  Documentation and examples available
  /spark - Initialise solver
  /spark/sources – Set sources (geojson)
  /spark/initialise_solver – Initialise solver
  /spark/run_solver – Run solver
  /spark/process_output – Custom post-processing
  /spark/raster_output – Get gridded output (tiff/json)
  /spark/vector_output – Get vector output (shp/geojson)
  Success codes 200/201

## Slide 60: SparkWeb
Spark server
Web API
  Services calls from SparkWeb
  Can be called directly to run simulations/serve outputs
  All models sent to server
API calls
  Documentation and examples available
  /spark - Initialise solver
  /spark/sources – Set sources (geojson)
  /spark/initialise_solver – Initialise solver
  /spark/run_solver – Run solver
  /spark/process_output – Custom post-processing
  /spark/raster_output – Get gridded output (tiff/json)
  /spark/vector_output – Get vector output (shp/geojson)
  Success codes 200/201
requests.post(f"http://localhost:{port}/spark/sources", headers=headers, json={
"sources" : {
"features" : [
{
"geometry" : {
"coordinates" : [ 150.342, -33.6 ],
"type" : "Point"
},
"properties" : {
"radius" : 120,
"time" : 0
},
"type" : "Feature"
}
],
"type" : "FeatureCollection"
}
})