## Slide 1
Dr Nathan Reid and Alex Hunt
Target 2023 Workshop: A practical guide to exploration hydrogeochemistry – Exploration Toolkit

## Slide 2
I would like to begin by acknowledging the Whadjuk people of the Noongar Nation as the Traditional Owners of the land that we’re meeting on today, and pay my respect to their Elders past and present.
Notes: Source: https://my.csiro.au/OrgInfo/Structure/Support/Indigenous/Resources

## Slide 3: Introduction
Exits, alarms etc
Introduce yourself and what experience you have in hydro or exploration space

## Slide 4: Introduction to hydrogeochemistry
What can it tell you about geology under cover, its strengths and weaknesses
Targeting mineral systems at regional and camp scales
How to collect consistent samples and the tools we can provide
What laboratory analyses are required and at what detection limits
How to check your data (QA/QC)
How to process data with XT Hydro
How to interpret your data within the regional context and tips for targeting

## Slide 5: Hydrogeochemistry – where it works
Tenement Selection
Greenfields Exploration
Provides baseline environmental information
Near Misses
Moving into thicker cover/basins
Indications of alteration
Detects known mineral systems
Detects weathering sulfides
Trialled on many commodities (Au, Base Metals, U)
Notes: Hydrogeochemistry is a regional detection tool. The sample spacing is generally not fine enough for ore body mapping but it can detect weathering sulfides at large scales and can determine what time of sulfides at smaller scales

## Slide 6: Field sampling
Key gear and steps
Field meta and chemical data collection
Youtube video available https://www.youtube.com/watch?reload=9&v=73iBM6zmoTs
FAIMS 2 and 3

## Slide 7: Field treatment
Eh, pH, temperature and conductivity measured immediately
Site details recorded
Water table depth
125 ml airtight sample collected for alkalinity
Filter (0.45 µm) ~ 300 ml
  100 ml for anions
  125 ml for cations (acidified - 2% concentrated HNO3)
1000 ml placed with C sachet and ~10 g NaCl
15+ min

## Slide 8: Equipment
Wear no jewellery
Or wear gloves
Cleanliness is key
Things which could be done in the field: Alkalinity titrations
Acidification
We don’t – carrying high purity acids in the field is problematic

## Slide 9: Boreholes
A mad array of bore types

## Slide 10: Pumps
Diversity of pumps

## Slide 11: Site measurements and observations
Water table
Location
Site observation
Contamination

## Slide 12: Sample collection
Bailing
From pump
Unorthodox

## Slide 13
Sampling log books, training guides, tablet field app

## Slide 14: FAIMS 2.6 Android app –a CSIRO twist on time savings
Developed through Macquarie University Archaeology, open source, now adapted for CSIRO protocol geochemical sampling (hydro, soil, vegetation and rocks)
Data Capture: auto GPS, dropdowns, tick boxes, photo tagging - Customizable
Field server: backs up multiple tablets in real time when in remote locations
Can be used for mapping and tracking
Robust field printed labels with data matrix – IGSN linked
Future: Set up for labs, new designed field server, auto upload to DAP, design your own module, linked to field devices (pXRF)
Notes: New sampling app – originally designed for hydro sampling – but now can be used for multiple media. Allows use of android tablet which is automatically linked to server in the vehicle –backs up data and contains large maps for download to tablet. Also can use maps – add polygons and sample points.

## Slide 15: Basic mapping functionality
Mapping: water samples overlying the MrVBF imagery (left). Soil samples overlying satellite imagery (right)

## Slide 16: Dropdown menus and field measurements
Water sample site information with dropdown options (left) and field chemical parameters (right).

## Slide 17: Time savings - optimisation
Soil sampling showing the field printed labels and data matrix for scanning into the application.

## Slide 18
Optimised Sampling
6 mins per site (+4 mins travel/refuel)
280 samples on 4 km spacing 80 x50 km area
5 sample types (soil, rock, vegetation)
IGSN/FAIMS – all integrated in tablets and QR code labels

## Slide 19: FAIMS 3.0: Electronic Field Notebooks
Shawn Ross, Penny Crook, Brian Ballsun-Stanton, Steve Cassidy, Jens Klump, Adéla Sobotkova and Nathan Reid

## Slide 20
The FAIMS Project is proud to partner with the following organisations:
We actively collaborate with researchers and experts from the following organisations:
The FAIMS 3.0 Electronic Field Notebooks project received investment (doi: 10.47486/PL110) from the Australian Research Data Commons (ARDC). The ARDC is funded by the National Collaborative Research Infrastructure Strategy (NCRIS).

## Slide 21: Introduction to the FAIMS Project
The Field Acquired Information Management Systems (FAIMS) Project began in 2012 as a national Australian information infrastructure project in archaeology.
Our core software FAIMS Mobile was developed for offline field data capture on Android devices.
Use expanded beyond archaeology to geoscience, ecology, ethnography, linguistics, oral history.
FAIMS Mobile is open-source (GPLv3); definition files shared on GitHub.
FAIMS Mobile has been customised for over 50 workflows at more than 40 projects.
FAIMS v2.6 is at the end of its useful life.
In 2020, ARDC Platforms and partners invested over $1.3 million to rebuild FAIMS using modern components.
Commercial open-source service (COSS) model for hosting services from 2023.

## Slide 22: FAIMS 3.0: Technical Specification
Cross-platform (React Native): Android 11+, Desktop and iOS
Web application to provide GUI to produce definition files.
‘Real’ user management and security (SSO, institutional logins).
NoSQL datastores (Apache CouchDB / PouchDB).
Definition files in JSON rather than XML.
Javascript map tilers (OpenLayers).
API development.
Interoperability with VLs / Gateways, domain repositories.
Plugin architecture.
See FAIMS3 Elaboration Report (https://zenodo.org/record/4616766) for more info. Or follow the building on GitHub: https://github.com/FAIMS/FAIMS3.

## Slide 23: Beta testing in Broken Hill (June 2022)
FAIMS 2.6 and FAIMS 3 being tested side by side in the Enhanced Mundi geochemistry project, Broken Hill June 2022. Left) Nathan Reid collecting soil sample metadata for Ultrafine+ sampling. Right) Chris Folkes (GSNSW) using FAIMS 2.6 and Nathan Reid using FAIMS 3 to test meta data capture while sampling waters at Broken Hill

## Slide 24: More Information
Contact
For more information contact info@faims.edu.au.
FAIMS 3.0 project website: http://faims.edu.au/.
FAIMS Project software, customisation library, and documentation can be found at: https://github.com/faims.
FAIMS Project OSF archive: https://osf.io/mqk45/.
FAIMS Project Zenodo community: https://zenodo.org/communities/faims/?page=1&size=20.

## Slide 25
Morning Tea

## Slide 26
Field sampling demo

## Slide 27: Analyses
A full suite is ideal
Anions – Cl, Br, F, SO4, NO3
Cations – Majors (Ca, Mg, Na, etc), Minors (Cu, Zn, W, U, REEs etc)
Alkalinity – HCO3 by titration
PO4, TN, DOC – from anions bottle
Precious metals – Au, Ag, Pt, Pd from carbon bottle
Isotopes – O, H from Anions bottle

## Slide 28: Gold hydrogeochemsitry
Au and precious metals are present naturally in concentrations of ng/L (ppt)
Pre-concentration steps are required to be able to accurately analyse especially in salty waters

## Slide 29
Pre-concentrate precious metals
Au and other precious metals Ag, Pt and Pd
Challenge associated to low concentrations in groundwater
Pre-concentration step added in the 1980s to overcome limits linked to analytical detection
Known volume of water = 1L
Adsorbent: Used to be
1.2 g of K- or Na-Cyanide
Now 10 g NaCl

## Slide 30
Lab data integration and QA/QC

## Slide 31: Lab integration
If you have sent samples off consistently this should be easily managed from the Sample IDs
Make sure duplicates and standards are interspersed at the same spots in the sample run to save time here

## Slide 32: QA/QC
Blanks – 1 in 20 in the field, 1 in 20 in the lab
Field duplicates – 1 in 20
Laboratory duplicates – 1 in 20
Certified Reference Materials (CRMs) – Matrix matching – 1 in 20

## Slide 33: QA/QC
Statistics and error calculations – choose your own adventure but I use % difference, 95% confidence and Half Relative Difference (HRD)
% difference error = ((assay1 - assay2) / maximum (assay1 or assay2)) x 100
Half relative difference = ((assay1 - assay2) / (assay1 + assay2)) x 100
Simple checks – Na vs Cl vs EC, S vs SO4, Sr OES vs Sr MS
where 1.96 is the 95th percentile of a normal distribution with a mean value of 0 and a standard deviation of 1, s is the standard deviation of all assay1-assay2 values, and n is the number of replicates.

## Slide 34: Data checking - QA/QC
Collate report details
Integrate detection limits usefully
If (early) datasets have higher detection limits remove data.
  Samples at detection will appear highly anomalous
Removal of spurious data, e.g.:
  pH values less than 2.5 and greater than 10.5
  Alkalinity > 0 when pH < 4.5
  Alkalinity > 50 when pH < 5 ...
  Si > 60 mg/L
  Have they corrected Eh to SHE (plot against pH should tell)
Check Ionic Balance ...
Correct for analysis of unfiltered waters

## Slide 35: Calculations
Ionic Balance – sum of ions (+ and -) should be zero
Contamination Factor/Value – accounts for organic contamination and pipe corrosion
TDS – from sum of ions
Ratios/Indices/Exploration indices – XT Hydro

## Slide 36: Contamination factor (shallow groundwater)
Fe, PO4, DOC, Mn, Zn: major difference between bailed & flowing samples  derive contamination parameter
Then group, from:
up to
98th percentile from flowing (uncontaminated) samples
Highly contaminated (5)
Bailed & uncontaminated (2)
Flowing (1)
5
This now goes to 6

## Slide 37: Culling contaminated data
Removed 4 and 5 from mapping

## Slide 38: Element index creation
Elements scaled: 0 -1, using 1st and 99th percentile of the data
Lithology Index (V, Cr, U)
Various exploration indices:
Sulfide deposits (Ni, VMS):
  FeS index = pH-Eh+Fe+Mn
  AcidS index = Mo+Ba+Li+Al
  Ni Min index = Ni+Co+W+Pt
  Ni Min – FeS
  Ni Min – AcidS
Au Min index = Au+Ag+As (also used (As+Bi)/2)
NO3 and SO4 excess and depletion based on ratios with Cl or Br
Mineral Saturation calculated using GWB (most useful for Uranium)
0
1

## Slide 39
Lunch

## Slide 40
Upload data
Map the columns
Process the indices
Explore the results
Tenement Selection
Greenfields Exploration
Provides baseline environmental information
Near Misses
Moving into thicker cover/basins
Indications of alteration
Detects known mineral systems
Detects weathering sulfides
Trialled on many commodities (Au, Base Metals, U)
Multi-element indices and element ratios from hydrogeochemistry data.

## Slide 41
Pre-Prototype
Prototype
Research Ready
Industry Ready
https://research.csiro.au/xt/
Notes: BACKGROUND CONTEXT
Strategic Project: Exploration Toolkit
New way of delivering science
Digital + Domain
Discovery Program’s Exploration Toolkit Project is split up into multiple sprints of work
It allows us to provide researchers within the program with Engineering and Data Science resources to help them progress their research through to industry ready products.
First significant sprint was working with Nathan Reid to improve how we produce our exploration indices from hydro data
An example of a industry ready product we have helped with is Data Mosaic which is used for interpreting drill hole data which is also being workshopped today by Dr June Hill

## Slide 42: Motivation: Why did we do this?
Existing process was slow.
Researchers wanted to spend less time processing data and more time investigating the results.
The complicated Excel Spreadsheet made it difficult to interrogate the implementation of the indices.
Onboarding new researchers was difficult.
Notes: What was our motivation?
Existing process – while it worked – was slow and manual
Too much time spent processing and preparing data
Not enough time spent investigating results and developing new ways of producing results
Training other researchers on how to do the process end-to-end was difficult
Easier training helps to prevent loss of knowledge

## Slide 43: Deciphering the spreadsheet: Before…
Notes: Reverse engineering constants
Tracing through spreadsheets to understand the process
Up on the screen is the Excel formula for the “Contamination Value” when formatted into something readable instead of the long string of text you normally see in Excel.
“Some people sure do go to extreme lengths to avoid writing code”

## Slide 44: Deciphering the spreadsheet: After…
Written in Python
Clear input arguments
32 Lines documenting it
10 Lines implementing it
Notes: 169 lines of formatted Excel formula becomes 45 lines of documented python
We can leverage the full python ecosystem like pandas, numpy, visualisation libraries, etc
If other researchers are doing the same thing, then it makes combining some of these techniques and processes far easier.
We can do more, with less effort.

## Slide 45: Welcome to Jupyter
Easy way to make the newly developed Python library accessible internally
Python Notebooks are great for demonstrating how to use the code
Easy to generate visualisations
Notes: Our hydro indices are now available as a Python library
At this stage we have a very solid prototype
We can now do the processing using Jupyter Notebooks and this can be done via the browser using the EASI Platform
We can use plotly, matplotlib, geopandas to visualise our data easily
Pandas lets us write our processed data to almost any format we want

## Slide 46: Next Step: Improve the User Experience
Upload data
Map the columns
Process the indices
Explore the results
Notes: We’ve wrapped the science in an easy to use web app
We’ve progressed to the Research Ready stage and our researchers don’t need to write a single line of python code anymore.
Researchers can upload their hydro data, map the columns from their data into the tool, process the data to get all the indices, and then visualise the results right there in the app and then download them as a csv, geopackage, Excel Spreadsheets, etc.
when they download that data it’s in a sane and consistent format which means if they want to pull it into another tool like ioGAS or ArcGIS they can do that without pulling their hair out.
Giving researchers more time to work on the interesting research challenges
After we have incorporated changes based on user feedback we can look at what would be required to make it available to the industry

## Slide 47: Future Work
Combine the process with other analytical tools/pipelines
Trialling other geochemical data types (soils, vegetation, etc)
Provide additional context by integrating with the Australian Continental Scale Hydrogeochemistry dataset
Current Features
Calculation of hydrogeochemistry describers
Calculation of element and exploration indices
Easy mapping of input data (csv/spreadsheets)
Geospatial visualisation of calculated indices

## Slide 48: XT Hydro
Free to sign up and try!
https://apps.exploration.tools/xt-hydro

## Slide 49: XT Hydro: Home

## Slide 50: XT Hydro: Upload
Option 1: Use the example dataset from East Isa
Option 2: Upload your own dataset (CSV, Excel)

## Slide 51: XT Hydro: Map Columns
Map the columns from your dataset to the schema used by XT Hydro
It will warn you about optional columns which are missing

## Slide 52: XT Hydro: Explore Data
Display output dataset with basic filtering/sorting
Download as CSV, GeoPackage, GeoJSON

## Slide 53: XT Hydro: Explore Data
If lat & long coordinates are available you can plot the data on a map

## Slide 54: Using XT Hydro - Compilation
Notes: Many data sources
Not just compilation! QA/QC and validation
Other datasets have more extensive element suites – different data densities
Our goal is to make as much of this data readily available in a consistent format that explorers can use

## Slide 55: Continental Scale Hydrogeochemistry
Finally a single dataset that we can use

## Slide 56: Interpretation
How do we visualise the data?
How do we interpret the data?
What tools are available?
  The Geochemist’s Workbench
  ioGAS
There is a nice set of useful data and an ArcMap file

## Slide 57: Continental Scale Hydrogeochemistry
Major parameters can show craton boundaries, major aquifer systems, and landscape system changes (Menzies line)
No other geochemical data set has this coverage and seamless integration

## Slide 58: Continental Scale Hydrogeochemistry
Different elements have different data densities

## Slide 59: Mineral Saturations
Calculations performed using GWB or PHREEQE (or others)
Can give potential that mineral phases are dissolving or precipitating (if present)
Very useful for U systems – primary (Autinite) or secondary (carnotite)
Can provide additional hints of mineral systems (not to be used in isolation)

## Slide 60
Water types: Piper Diagrams
Can be easily constructed in IoGas.
Helps to pick different aquifers within a region
Once clusters of samples are identified – this can be used as a baseline for checking anomalism or lithology changes

## Slide 61
Metal anomalism and water types

## Slide 62: Isotopes – O and D
Continental evaporation trend pervasive
Variations from this trend can indicate different water sources
Isotope index coming soon to XT hydro

## Slide 63: Lithology mapping

## Slide 64: Scale is Critical
  What is the scale of your system, and its sub-components?
  What is the scale of the dispersion?
  Which elements work better a varying scales, with varying cover?
  The same element / or index can be telling different things at different scale:
    Sr:Ca high Sr is denoting acid vs basic rocks at > km scale, and mineral system effects at < 100 m scale
    At < 100 m scale SO4 anomalism is correlated with sulfides. At > km scale with fracturing and groundwater upwelling, and potentially with large Iron systems

## Slide 65: Relevance of scale
Left) Continental scale SO4:Cl ratio, showing large scale lithology changes and Right) at smaller scale showing areas of weathering sulfides at the Jaguar/Teutonic Bore/Bentley VHMS ore bodies, this data was collected prior to the Bentley discovery. Far Right) new data from the Dugald River region highlighting anomalies near mines

## Slide 66: Element Ratios - examples
KNaSW = [2 x (K - 0.0363 x Na)]/[0.0363 x (Na + 500)] ... Na < 500 mg/L
= [K - 0.0363 x Na]/[0.0363 x Na] ... Na ≥ 500 mg/L
SrCaSW = [2 x (Sr - 0.0195 x Ca)]/[0.0195 x (Ca + 20)] ... Ca < 20 mg/L
= [Sr - 0.0195 x Ca]/[0.0195 x Ca] ... Ca ≥ 20 mg/L
SO4ClSW = [2 x (SO4 - 0.1396 x Cl)]/[0.1396 x (Cl + 500)] ... Cl < 500 mg/L
= [SO4 - 0.1396 x Cl]/[0.1396 x Cl] ... Cl ≥ 500 mg/L

## Slide 67: Ca excess (to Sr)
Maps most greenstones in the Yilgarn
There is more Ca and Sr data across the country than there is Cr, V, Ni etc

## Slide 68: Lithology mapping (under cover?)

## Slide 69: Uranium systems

## Slide 70: Secondary Uranium - acid/saline systems
Acid groundwaters interacting with granites and other felsic rocks can generate extremely high dissolved U
These groundwaters are also saline, high Ca, Fe, Pb etc
Ca (& Fe)  low dissolved PO4
Fe (& Pb) (& low pH)  low dissolved V
Uranium will only be immobilised by reduction  lignites or sulphides (e.g., Beverley)

## Slide 71: Secondary Uranium - neutral/fresh systems
Despite lower uranium fluxes, much more prospective for secondary uranium
Unravelling complex direct, and indirect controls
Low Ca  high dissolved PO4, and higher dissolved U
Mixing with oxidised V-containing groundwaters  Carnotite. Observed using Saturation analyses
Major variation in size
Able to see mineralised areas at > 4 km sampling

## Slide 72: Example Uranium Chemistry
0
2
4
6
8
10
12
14
–.5
0
.5
1
pH
Eh (volts)
Carnotite [KUO2VO4]
Coffinite [USiO4]
25°C
[U] = 10-9 M
[V] = 10-15 M
[P] = 10-5 M
[K] = 0.001 M
[Si] = 0.0015 M
[C] = 0.002 M
(T = 25 °C, P = 1.013 bars)
UO2(CO3)2
2-
UP2O7(C)
UO2(CO3)3
4-
UO2HPO4
0
UO2(H2PO4)2
0
UO2(H2PO4)(H3PO4)+
Geochemists Workbench ® (thermo.com.v8.r6+.dat)

## Slide 73: Uranium solution chemistry

## Slide 74: Carnotite Saturation + U:Th Radiometrics

## Slide 75: Base metals – Its all about pathfinders
All of these have several examples we could look at across Australia, or have a play with the continental data at your leisure

## Slide 76: Direct metals not great indicators: Jaguar area
Cu (mg/L)
< 0.003
0.004
0.006
0.055
0.30
Geology
Felsic rocks
Granitic rocks
Mafic intrusive
Mafic rocks
0.00 - 0.02
0.02 - 0.04
0.04 - 0.08
0.09 - 0.13
0.13 - 0.18
0.19 - 0.37
0.40 - 0.84
0.93 - 18
Geology
Felsic rocks
Granitic rocks
Mafic intrusive
Mafic rocks
0
0.5
1
Kilometres
Dissolved base metal data very patchy! – If you have any at all in some areas
Zn (mg/L)
0
0.5
1
Kilometres

## Slide 77: Ni
Direct detection in acid or neutral waters
Its just the size of the footprint that changes
Ni, Co, Cr, W, PGEs

## Slide 79: Using metals etc to find sulphides: FeS Index (pH-Eh+Fe+Mn)
Harmony System
NW sulphide area - strong anomaly
Southern ore body – weak. Implies less Fe-rich S
Emphasizes barren over mineralised sulphides
0
1
2
3
4
0.5
Kilometres
0
1
2
3
4
0.5
Kilometres
pH
-
Eh+Fe+Mn
Index
0.72
-
0.79
0.59
-
0.72
0.44
-
0.58
0.29
-
0.44
0.00
-
0.29

## Slide 80: Finding Ni sulphides - Harmony
NiS Indicators
Southern deposit strongly delineated
Northern deposit moderately delineated
West only weakly anomalous
0
1
2
3
4
0.5
Kilometres
0
1
2
3
4
0.5
Kilometres
Ni+Co+W+Pt
Index
0.76
-
0.80
0.58
-
0.75
0.42
-
0.58
0.27
-
0.42
0.00
-
0.26
NiS Index (Ni+Co+W+Pt)

## Slide 81: Finally correct for NiS (NiS – FeS) .
Harmony deposit strongly anomalous
Anomalies along strike
Northern prospect delineated
West less anomalous
0
1
2
3
4
0.5
Kilometres
0
1
2
3
4
0.5
Kilometres
Min
-
FeS
Index
0.15
–
0.37
0.00
-
0.15
-
0.15
–
0.00
-
0.30
-
-
0.15
-
0.75
-
-
0.30

## Slide 82: Various Indices  targeting at Regional & Prospect Scale
additional anomalies along strike
Works very well at 10m – km scale
250000
300000
6850000
6900000
6950000
7000000
0
10
20
km
NiS Index
> 0.85
0.75 - 0.85
0.60 - 0.75
0.40 - 0.60
< 0.40
Honeymoon Well
Yakabindie
Waterloo
Jaguar
270000
6925000
6930000
6935000
0
1
2
km
Harmony Ni deposit
265000

## Slide 83: Pb-Zn
Direct detection and a swathe of associated pathfinders
However, ore is often not very soluble
Carbonates are easier than sulfides
Pb, Zn, Cd, Tl

## Slide 84: Cu
Cu – direct in acid waters, its all about proxies and associated elements in neutral waters
  Cu is adsorbed onto Fe-Oxides/Clays readily
Acid waters – Cu, Au, Fe – but hard to pick against a high background
Neutral waters –Au, As, Fe, Mo, W, S isotopes, maybe Cu
Bottom line – look for sulfides, then try and work out what type you have

## Slide 85: Sulfide detection
Waters around sulfides can have one or more of the following properties:
1. Low Eh, and/or low O2 saturation;
2. Moderate to extremely high dissolved Fe content;
3. Low pH;
4. High concentrations of elements normally characteristic of acid lithologies (Ba, Li, Mn, Mo, V, W);
5. More rarely, detectable Al and REE (La, Ce, etc.), even in groundwater above pH 6, despite these elements normally only being soluble below pH 5.5.

## Slide 86: Acid production
H+/Metal
(O2 oxidant)
H+/Metal (NO„ oxidant)
-2
2
Pyrite
Pyrrhotite
Chalcopyrite
Acanthite
Sphalerite
Chalcocite
Villamaninite
Covellite
Galena
-1
0
1
3
4
1
Using pH alone will more easily detect pyrite than other sulfides

## Slide 87: Modelling Sulfide Systems – Example from NiS ore bodies
0
400
800
1200
1600
0
1
2
3
4
5
6
SO4 (mg/L)
Br (mg/L)
Enrichment
Depletion
Pentlandite  violarite
Pyrrhotite  /pyrite/hematite with SO42- as oxidant
2FeS + 0.4SO42- + 1.6H2O  0.8Fe(OH)3 + 1.2FeS2 + 0.8OH-
Violarite  Ni silicate
Pyrite  Fe oxide with NO3- as oxidant
2FeS2 + 6NO3- + 4H2O  4Fe(OH)3 + 4SO42- + 3N2 + 2H+

## Slide 88: SO4, NO3 and FeS Indices – Jaguar VMS
SO4 Anomaly
High
Medium
Low
None
Geology
Felsic rocks
Granitic rocks
Mafic intrusive
Mafic rocks
FeS Index
0.72-0.79
0.59-0.72
0.44-0.58
0.29-0.44
0.04-0.29
Geology
Felsic rocks
Granitic rocks
Mafic intrusive
Mafic rocks
0 - 2
3 - 4
5 - 20
21 - 50
51 - 80
81 - 135
Geology
Felsic rocks
Granitic rocks
Mafic intrusive
Mafic rocks
Known ore bodies
Fe gossan
Exploration sites
0
0.5
1
Kilometres
0
0.5
1
Kilometres
0
0.5
1
Kilometres
NO3 (mg/L)

## Slide 89: Deep Processes - Pyrrhotite/pentlandite alteration
0
5
10
15
20
Pyrrhotite
Pentlandite
Pyrite
Magnetite
Violarite
0
0.2
0.4
0.6
0.8
1
Reaction progress
Minerals (grams x 100)
Hematite
2FeS + 0.4SO42- + 1.6 H2O Ý 0.8Fe(OH)3 + 1.2FeS2 + 0.8OH-
Geochemists Workbench ® (thermo.com.v8.r6+.dat) + Warner et al. (1996)
This will cause SO42-, HCO3- and NO3- DEPLETION in deep groundwaters contacting sulphides

## Slide 90: Shallow Processes – Pyrite / violarite oxidation
0
50
100
150
200
Minerals (grams)
Ni2SiO4
Violarite
Pyrite
Hematite
0
0.2
0.4
0.6
0.8
1
Reaction progress
Polydymite
Geochemists Workbench ® (thermo.com.v8.r6+.dat) + Warner et al. (1996)
SO42- ENRICHMENT and NO3- DEPLETION in shallow groundwaters contacting sulphides

## Slide 91: Gypsum Saturation
Gypsum SI is another way that excess sulfate can be expressed
And Ba, Barite, Jarosite and Alunite

## Slide 92
Mangroves?
Cairn Mining
Honeymoon Well
Mines
Erlistoun
Sth Windarra Mine
Mines
Mines
Teutonic
Mine
Yeelirrie
Mines
“Diorite Well”
Mt Magnet
Paulsen
Newman
Plutonic
Peak Hill
Jundee
Mine
Mine
Mt Keith
Mine
Leonora
Murrin
Sunrise
Garden Well
Mine
Mines
?
?
?
Anomalous Sulfate - Exploration
Take away SO4 from gypsum and alunite effects
This excess SO4 shows reasonable spatial correlation with mineralised systems
Uses major element data alone
Sulfides  Oxides e.g.:
FeS2  Fe(OH)3 + 2SO42-
Sulfide Alteration, e.g.:
FeS + 0.2SO42-  0.6FeS2 + 0.4Fe(OH)3
+
-

## Slide 93: Gold
Least amount of data available
Need preconcentration step and specific analysis
Direct detection in acid or neutral waters
Key pathfinders: Au, Ag (primary), As, Sb, Bi, W, Mo, Te

## Slide 94
Gold exploration
Gold Exploration
Au is the best pathfinder
Challenges:
Not part of traditional water analysis (fewer data points)
“Nugget” effect still possible
Detection limits

## Slide 95: Gold
This is a compilation and ~20 years of work/sampling
Notes: Raw Au concentrations pick up most major Au systems – when samples are within ~1 km

## Slide 96: Gold hydrogeochemsitry
Anomaly to background contrast in all primary pathfinders is strong

## Slide 97: Gold hydrogeochemsitry
Notes: Less data as analytical accuracy was not good enough in the older data

## Slide 98: Indices from XTHydro - AuMin
AuMin = Normalised (Au+Ag+As)

## Slide 99: Gold Case Studies - Agnew
Notes: Primary Au near surface, everything shows up as anomalous

## Slide 100: Gold Case Studies – Garden Well
Notes: Primary mineralisation at depth, secondary enrichment near surface – this is what is expressed in the groundwater (very shallow)

## Slide 101: Key Points
Au can be detected in natural waters but they are at low conc
Pre-concentration is necessary – INAA or ICP-MS analysis
Au systems often (but not always) have associated pathfinders in waters (Ag, As, Sb, W, Mo)
The AuMin index can improve halo size but can miss secondary Au
More data is always wanted and needed

## Slide 102: Li
Still early days
We don’t have key data around known mineral systems
Many anomalies can be generated but what do they mean
More research required

## Slide 103: Rare Earth Elements
In acid waters REEs are in high concentrations everywhere
  So what is anomalous? What is a trap for mineralisation
In neutral waters most samples are below detection
  But using the U exploration methods could pay off

## Slide 104
Archaean Lode Gold: 10 km’s  10 m’s
Calcrete Uranium: 10 km’s  100 m’s
(Any) Sulfides: km’s  100 m’s
Ni-S: 100 m’s  10 m’s
VHMS: km’s  10 m’s
IOCGs: alteration systems at km’s
Cu Porphyrys: km’s  100 m’s
Effective for residuum in (semi-)arid Australia
Harder for acid and saline areas of southern Australia – backgrounds are so much higher
Hydrogeochemistry Bottom Line (Australia)
  Based on size of mineral system / anomalism for various elements

## Slide 105: Outputs

## Slide 106: So how can hydro help exploration?
The regional data can provide new areas of interest for picking tenements
New samples collected can be placed in context with the regional background – please talk to us
Understanding hydrogeochemical signatures of lithology and mineralisation at both regional and camp scales
Support using the FAIMS field app for sample collection

## Slide 107: Hydrogeochemistry
New or Existing projects
Field apps/tools
Quality time for interp. & interrogation
Baseline integration
Come talk to us
Faster processing
Continental Hydrogeochemistry

## Slide 108
Thank you
Mineral Resources
Nathan Reid and Alex Hunt Nathan.Reid@csiro.au
Alex.Hunt@csiro.au